The filtering of the meshes:

Before decimation:
- It might be necessary to split the mesh and clean elements separately.
- Selection→ Select non Manifold Edges
- Selection→ Delete selected vertices
- Selection→ Select non Manifold Vertices
- Selection→ Delete selected vertices
- Quality Measure and Computation →Compute Topological Measures
- Selection→ Delete selected vertices
- Remeshing, Simplification and Reconstruction → Close Holes
30mm used.
- Cleaning and repairing →Remove Unreferenced Vertices
- Quality Measure and Computation →Compute Geometric Measures
- Quality Measure and Computation →Compute Topological Measures

Decimation:
- Remeshing, Simplification and Reconstruction → Simplification: Quadric edge collapse decimation
Comments: it is only possible to choose number of faces, not vertices. A loop will be	applied to repeat until the the given number is obtained. Can be used with Percentage reduction to get the correct number of vertices (6 relevant places!)
- Percentage reduction: to be computed, in case_01: 0.050486
- Quality threshold: 1.0
- Preserve Boundary of the mesh: Off
- Preserve Normal: On
- Preserve Topology: On
- Optimal position of simplified vertices: On
- Weighted Simplification: Off
- Planar Simplification: On
- Post-simplification cleaning: Off
- Simplify only selected faces: Off

TODO:
The point correspondence must be established between meshes, then they can be applied to the atlas class.

Remeshing:
- Clean the non manifold vertexes with selection of non manifold edges and deletion (filter doesn’t work!) then fill holes and check the geometry and topology. SAVE!
- Use one of the subdivision filters – all except midpoint and catmull-clark (former is VTK version of it and latter builds quads)
- Results:
- LS3 loop works better than loop
- Setting the length to 0 yields good results
- Enhanced regularization helps
- It is poossible to select the faces with concrete edge lengths to run decimation on them. With a proper threshold, it could lead to nice and uniform meshes.
- Butterfly creates patches on length 0, but it works nicely on 2
- Use the Hausdorff distance to estimate quality and choose the best solution
- Remeshing, Simplification and Reconstruction → Laplacian smooth (surface preserve):
- play with angle and number of iterations

Old
- Remeshing, Simplification and Reconstruction → Uniform Mesh Resampling
- Precision ‘world unit’: 0.5 (mm)
- Offset ‘world unit’: 0
- Clean Vertices: On
- Discretize: Off
- Multisample: On
- Absolute Distance: Off

Cleaning resampled mesh:
- Cleaning and repairing → Remove Isolated Pieces (wrt Diameter)
10% used, might be smaller if mesh is divided into segments.